## Slide 1: An Amicus Brief:
Robert Bradford
Advanced Photon Source Detectors Group
Argonne National Laboratory
15 November, 2013
3D-ASICS for X-ray Science

## Slide 2: A little background: X-ray Science
Advanced Photon Source:
  Light source up the road…
  Largest user facility in the US
  Very broad scientific user community – biology, chemistry, material science, physics…
  ~80 different experimental end-stations on ~30 beamlines
Many simultaneous experiments using variety of techniques
Detector needs very diverse, no “one-size-fits-all” solutions
  Experiments compromise between speed (frame rate), temporal resolution, energy resolution, spatial resolution, and dynamic range
  Widely acknowledged that detectors do not meet current needs

## Slide 3: A little background: ASICS in X-Ray Detection
Custom ASICs have become commonplace in synchrotron science during the past ~7 years:
  “Hybrid pixel detectors” for x-rays are natural extension of silicon detector work done in HEP
  Much of work done in Europe building off of LHC
Many commercial detectors based on single photon counting:
  PSI Pilatus – 2006
  Licensed to Dectris – very successful
  Many efforts in Europe
Most important detector at APS for past ~5 years
  Easy to use, robust, good SNR…
  ~50 systems costing $10-15M
C. Broenimann, et al. J. Synchrotron Rad. (2006), 13, 120-130.
http://www.azonano.com/article.aspx?ArticleID=2631
http://lima.blissgarden.org/camera/pilatus/doc/index.html
http://www.imxpad.com
http://www.amscins.com
Notes: Probably the most important detector at the APS right now.

## Slide 4: Simple Example - AGIPD
Analog detector with integrating logic for European XFEL
Adaptive gain:
Sensitivity to single photons or 104 photons
Analog storage –
Buffers 352 images to permit 4.5 MHz frame rate.
ADC handled off chip.
http://photon-science.desy.de/research/technical_groups/detectors/projects/agipd/

## Slide 5
http://aps.anl.gov/Users/3Way/presentations/Graafsma.pdf
Platform being refined for gapless coverage.
TSV being explored with existing Medipix3 Chips
Next iteration of AGIPD: 3-tier ASIC

## Slide 6: 3D ASICS
Huge potential for impacting x-ray science
Seen as a key step forward for x-ray detectors:
  Edge-less sensors without gaps in coverage
  Smarter pixels for technique specific detectors with fast in-ASIC analysis capability
  Spatial resolution is key to many experiments
    Hybrid pixels typically ~50-200 mm
    CCDs and CMOS can provide 5-30 mm pixels
Overcomes key compromises
  3D ASICS: intelligent pixels + spatial resolution + high frame rates +???