## Slide 1
Cosmic Background Neutrino Decay Search
– COBAND Experiment –
Continuous Spectral Measurement in Far-Infrared Region using STJ
Shin-Hong Kim （University of Tsukuba, TCHoU）
for COBAND collaboration
at Fermilab
November 21, 2017

## Slide 2: COBAND (COsmic BAckground Neutrino Decay) Collaboration
S.H. Kim, Y. Takeuchi, K. Takemasa, K. Nagata, K. Kasahara, S. Yagi, R. Wakasa, R. Senzaki,
K. Moriuchi, C. Asano, T. Iida (University of Tsukuba),
S. Matsuura (Kwansei Gakuin University),
H. Ikeda, T. Wada, K. Nagase, S.Baba (JAXA),
Y. Arai, I. Kurachi, M. Hazumi (KEK),
T. Yoshida, M. Sakai, T. Nakamura (University of Fukui),
Y. Kato (Kindai University),
K. Kiuchi, S. Mima (RIKEN),
H. Ishino, H. Kibayashi (Okayama University),
S. Shiki, G. Fujii, M. Ukibe, M. Ohkubo (AIST),
S. Kawahito (Shizuoka University),
E. Ramberg, P. Ruvinov, D. Sergatskov (Fermilab),
S.B. Kim (Seoul National University)

## Slide 3: Motivation of Search for Cosmic Background Neutrino Decay
As the neutrino lifetime is very long, we need use cosmic background neutrino to observe the neutrino decay. To observe this decay of the cosmic background neutrino means a discovery of the cosmic background neutrino predicted by cosmology.
Left-Right symmetric model predicts the neutrino lifetime larger than 1017 year while the standard model predicts 2 x 1043 year.
Measured neutrino lifetime limit τ > 3 x 1012 year.
Only neutrino mass is unknown in elementary particles. Detection of neutrino decay enables us to measure an independent quantity of Dm2 measured by neutrino oscillation experiments. Thus we can obtain neutrino mass itself
from these two independent measurements.

## Slide 4: Big-Bang Cosmology and Cosmic Background Neutrino (CνB)
A few seconds after Big Bang → Cosmic Background Neutrino (CνB)
became free.
300,000 years after Big Bang → Cosmic Microwave Background (CMB)
became free.

## Slide 5
Large Scale Structure of the Universe and CνB
Large Angular scale(180°/l) Small
Temperature fluctuation of CMB observed by Planck satellite
Theoretical prediction on Power Spectra of the angular correlation of the CMB temperature fluctuation （depending on the neutrino mass）
Angular correlation at high temperature
High Temperature ＝ High Galaxy matter density
CνB exists → large angular correlation at high angle higher neutrino mass → larger angular correlation at high angle
Ref. J. Lesgourgues, S. Pastor Phys. Rep. 429 (2006) 307
Decision Factor of Temperature Fluctuation：
Dark matter, Dark energy, Neutrino
↓
Matter density
or Large scale structure of the Universe
no n’s
mn = 0
Smn = 1eV

## Slide 6: Photon Energy from Neutrino Decay
m3=50meV
m1=1meV
m2=8.7meV
E =4.4meV
E =24meV
Sharp Edge with 1.9K smearing
Red Shift effect
dN/dE(a.u.)
Photon energy distribution
meV]
E =24.8meV
()
()
()
Neutrino oscillation results
Space observatory results（ Planck+WP+highL+BAO）
50meV<<87meV
  14~24meV (51~89m)
Neutrino decay

## Slide 7
Cosmic Infrared Background Radiation

## Slide 8: Cosmic Infrared Background Observation by COBE
Infrared light from star-heated dust in the Milky Way
January 1998 (Press Release): COBE (Cosmic Background Explorer) announced the first observation of the cosmic infrared background (CIB)
Infrared light emitted from interplanetary dust heated by the Sun (zodiacal light) : S-shaped

## Slide 9: Cosmic Infrared Background Observation by COBE
(Top) Observed Sky at λ = 60 μm(blue), 100 μm (green) and 240 μm(red).
Horizontal band corresponds to Infrared light from interstellar gas in the plane of our Milky Way Galaxy. The blue S-shaped region corresponds to Infrared light from interplanetary dust in the solar system called zodiacal emission.
(Middle) After removing the zodiacal emission.
(Bottom) After removing the infrared light from our solar system and Galaxy at λ = 240μm.
COBE announced that they observed the extragalactic residual infrared light called “Cosmic Infrared Background” at the 240 and 140 micrometer wavelength.

## Slide 10: Cosmic Far-Infrared Background Observation by AKARI
November 2008 : AKARI ( JAXA Infrared Imaging Satellite) observed 64,000 stars and galaxies at wavelengths of 65, 90, 140 and 160 μm. Made a whole sky map. They extracted CIB map from this observation.
λ = 90 μm
AKARI whole sky map in far-infrared region

## Slide 11: Photon Energy Spectrum from Outer Space
CMB
Zodiacal Emission
Zodiacal Light
Interstellar Dust
Integrated
Star Light
Diffuse
Galactic Light
wavelength [m]
E [meV]
Surface brightness I [MJy/sr]
AKARI
COBE
Integrated flux from galaxy counts
Galaxy evolution model
CIB measurements
( AKARI,
 COBE)
There was an excess of the CIB measured by COBE and AKARI over the prediction by galaxy evolution model.
Sources at FIR: dusts of far galaxies or far blackhole, or CνB decay ?
Sources of NIR: first-generation stars Ly-α ?

## Slide 12: Our paper published in JPSJ on Jan. 18th, 2012
12
Search Region: λ＝ 35～250μm （Eγ ＝ 35～5meV）
In Rocket experiment, λ＝ 40～80μm （Eγ ＝ 31～15meV）

## Slide 13: Lower Limit of Lifetime from the Energy Spectrum Fit to the CIB measured by COBE and AKARI(1)
Using the CIB at 60, 100（ ApJ, 544, 81, 2000 ), 140, 240 µm ( ApJ, 508, 25, 1998 ), 65, 90,
140, and 160 µm ( arXiv:1002.3674, 2010 ), the photon energy spectrum from neutrino radiative
decay gives a lifetime lower limit of 2.4 x 1012 year at 95% C.L. for m3 = 0.05eV and m2 = 0.01eV. ( My calculation )
χ2= 6.6
τ= (2.8±0.2) x1012 year
= (0.85±0.06) x1020 sec
Photon Energy (eV)
νdI/dν (nW m-2 sr-1)

## Slide 14: Lower Limit of Lifetime from the Energy Spectrum Fit to the CIB measured by COBE and AKARI(2)
ν3 mass (eV)
ν3 lifetime limit at 95% C.L. (year)
Δm232 = 0.00243 eV2
2.4 x 1012 years
We need 5 order improvements.

## Slide 15
Cosmic Background Neutrino Decay Search
(COBAND)

## Slide 16: Signal of Cosmic Background Neutrino Decay and its Backgrounds
CMB
Zodiacal Emission
Zodiacal Light
Interstellar Dust
SL
DGL
wavelength [m]
E [meV]
Surface brightness I [MJy/sr]
AKARI
COBE
Integrated flux from galaxy counts
Galaxy evolution model
CIB measurements
( AKARI,
 COBE)
By measuring the energy spectrum of the Zodiacal Emission with the CνB decay continuously, we can see the CνB decay signal as a high energy cutoff.
Rocket experiment coverage (λ＝40～80μm)
High Energy Cutoff (25meV)

## Slide 17: COBAND (COsmic BAckground Neutrino Decay Search) Experiment
JAXA Rocket CIB Experiment
（Feb 2, 1992）
  Satellite experiment after 2020 → sensitivity of τ(ν3) ~1017year
  STJ using Hafnium: Hf-STJ for satellite experiment ( S. H. Kim et al. JPSJ 81,024101 (2012)）
    : Superconducting gap energy for Hafnium
    for 25meV photon: if Fano-factor is less than 0.3
Rocket Experiment Plan: 5minutes data acquisition at 200 km height in 2019.
Improve the current limit of lifetime τ(ν3) by two orders of magnitude ( ~1014years).
Superconducting Tunneling Junction (STJ) detectors in development
  Array of 50 Nb/Al-STJ pixels with diffractive grating covering
3He sorption 0.4K
FOV = 0.006°ｘ 0.05°

## Slide 18: Zodiacal Emission
Thermal emission from the interplanetary dust cloud
, ,
[Js], [m/s], [m]
Zodiacal Emission(ZE) is overwhelmingly dominating. Here we consider only ZE as the background.

## Slide 19: Zodiacal Emission
Surface brightness I [W/m2/sr]
1m
10m
100m
1mm

## Slide 20: Discovery Potential for Neutrino Decay
Create a pseudo-data for ND and ZE expectation on assumption of 3 mass and lifetime: Nobs(mtrue, true)
Calculate expected distribution of ND+ZE on assumption of 3 mass and lifetime: Nexp (m, )
Calculate likelihood of the pseudo-data as a function of the decay width for each neutrino mass
Obtain the most probable decay width and its significance
m(3)=50meV
yrs
yrs
Significance=3.9

## Slide 21: Sensitivity to Neutrino Decay
Parameters in the rocket experiment simulation
telescope diameter: 15cm
50-column (: 40m – 80 m)  8-row array
Viewing angle per single pixel: 100rad  100rad
Measurement time: 200 sec.
Photon detection efficiency: 100%
If 3 lifetime were 2  1014 yrs, the signal significance is at 5 level
50 60 70 80
λ（μm)
Zodiacal Emission
Excess due to Neutrino Decay

## Slide 22: COBAND Experiment Sensitivity to Neutrino Decay
S.H.Kim et. al (2012)
Mirizzi et. al (2007)
LRS =0.02, M(W2)=750GeV
m312 = 2.510-3eV2
mi < 0.23eV
COBAND Rocket Experiment
x100 Improvement !

## Slide 23: R&D Status of Superconducting Tunnel Junction Detector for COBAND experiment

## Slide 24: STJ (Superconducting Tunnel Junction）Detector
At the superconducting junction, quasi-particles over their energy gap go through tunnel barrier by a tunnel effect. By measuring the tunnel current of quasi-particles excited by an incident particle, we measure the energy of the particle.
Superconductor / Insulator / Superconductor Josephson Junction
S
I
S
2Δ
Quasi-particles
Incident Particle
Cooper Pairs
current-voltage (I-V) curve for STJ
Leakage current
( Dynamic resistance Rd in |V| < 2Δ/e)
Josephson Current
Critical current Ic
Energy gap Δ

## Slide 25: STJ Energy Resolution
Δ: Band gap energy
F: Fano factor (= 0.2)
E: Incident particle energy
Tc : Critical Temperature
Operation is done at a temperature around 1/10 of Tc
STJ Energy Resolution
We reported that Hf-STJ worked as a STJ in 2011.
Material |  | 
Niobium | 9.20 | 1.550
Aluminum | 1.14 | 0.172
Hafnium | 0.13 | 0.021

## Slide 26: Nb/Al-STJ Photon Detector
Quasi-particles near the barrier can mediate Cooper pairs, resulting in true signal gain
  Bi-layer fabricated with superconductors of different gaps Nb>Al to enhance quasi-particle density near the barrier
  Nb(200nm)/Al(70nm)/AlOx/Al(70nm)/Nb(100nm)
  Nb/Al = 0.57meV
Number of Quasi-particles in Nb/Al-STJ
GAl : Trapping Gain in Al(~10)
E0 : Photon Energy
Δ : E-Gap in superconductor
For 25meV single photon
Nq = 10
= 250 e
300nm
Back tunneling Effect → Trapping Gain
Response of Nb/Al-STJ to visible laser light pulse
(λ=465nm) at 350mK

## Slide 27: Leakage Current of Nb/Al-STJ
Temperature Dependence of Leakage Current
  Leakage current Ileak is required to be below 0.1nA to detect a single far-infrared photon (λ= 40 -80μm) .
  In 2014,
  AIST group joined us and produced Nb/Al-STJ with AIST CRAVITY processing system.
  Leakage current has satisfied our requirement of 0.1nA .
Ileak = 0.2nA
at 300μV
below 400mK
50μm x 50μm
by T. Fujii (AIST)
STJ size | # of samples | Ileak at 0.3mV
50 x 50μm2 | 18 | 224±29 pA
20 x 20 μm2 | 7 | 39±13 pA
10 x 10 μm2 | 20 | 14±7 pA
Ileak∝

## Slide 28: Test Results of Nb/Al-STJ with Far-Infrared laser
Nb/Al-STJ Response to Far-Infrared Laser
20m-square Nb/Al-STJ made at AIST CRAVITY system
Laser light was turned on and off with a chopper at a frequency of 200Hz. Measured the change of the I-V curve between the laser on and off to be 50~100nA in current.
Far-Infrared Laser at University of Fukui（=57.2m）

## Slide 29: R&D Status of SOI Cryogenic Preamplifier for STJ

## Slide 30
R&D of SOI-STJ Detector
To improve the signal-to-noise ratio and to make multi-pixel device easily, we made a SOI-STJ detector where we processed Nb/Al-STJ on a SOI transistor board.
    FD-SOI (Fully Depleted Silicon-On-Insulator) device was proved to operate at 4K by a JAXA/KEK group (AIPC 1185,286-289(200 FD-SOI 9)). It has the following characteristics:
    low-power consumption, high speed, easy large scale integration and suppression of charge-up by high mobility carrier due to thin depletion layer(～50nm).
    FD-SOI -MOSFET
    ～50nm
    Nb/Al-STJ
    SOI preamplifier

## Slide 31
Performance of STJ and SOIFET in SOI-STJ detector
r0
500uV /DIV.
1μs /DIV.
Signal
(1.5μs)
We observed the signal of Nb/Al-STJ processed on the SOI board to 465nm laser pulse at 700mK.
We confirmed that the SOI-FET work as a preamplifier with a gain of 8.7 at 4K up to 100kHz.
GAIN 8.7 @ LHe temp.

## Slide 32
SOI Cryogenic Amplifier
Amplification
Replace the resistance by a SOIFET as a current source (M2).
Feedback
Use the feedback between the drain and the gate of M1 to apply a stable bias voltage (M3).
Buffer
Add the follower to reduce the output impedance (M4 and M5).
Designed the ratio (W/L) to set the
operation power consumption below 120μW.
This SOI amplifier board was made by LAPIS semiconductor company.
SOI-STJ4 (the 4th prototype)
Vb
Vss1
V5
Vss2
Vdd1
Vdd2
V2
V3
INPUT
OUTPUT
We updated the SOI cryogenic Amplifier for Nb/Al-STJ.

## Slide 33
Test Results of the SOI Cryogenic Amplifier
Gain vs. Frequency
at 300mK
Amplifier + Buffer
Input and Amplified Output
Amplified Output (50mV/div)
Input (1mV/div)
Input
Output
Time scale 2ms/div
Gain of 80 was achieved for a signal frequency
up to 400kHz signals at 300mK.
400kHz

## Slide 34: Setup of STJ Signal Amplification with the SOI Cryogenic Amplifier
20m-square Nb/Al-STJ with SOI-STJ4 amplifier through 4.7μF capacitance.
Input impedance of the SOI amplifier is about 20kΩ.
  STJ operation at a constant current mode.
  STJ bias cable capacitance is around 1nF：Z=160Ω for 1s signal.
STJ
10MΩ
T~350mK
465nm laser through optical fiber
GND
Vss
Vdd
4.7F
Input Monitor
Output
STJ
SOI
4.7F
SOI Amplifier
3He sorption refrigerator

## Slide 35
STJ signal amplified with the SOI cryogenic preamplifier
Nb/Al-STJ laser light response signal was amplified with this SOI cryogenic preamplifier at 350mK.
Amplification Gain : 70
S/N improved by a factor of 2
Development of the SOI cryogenic preamplifier is now moving to the stage of the final design for COBAND experiment.

## Slide 36: R&D Status of Hf-STJ

## Slide 37
R&D Status of Hf-STJ
Goal: Measure energy of a single far-infrared photon for neutrino decay search experiment within 2% energy resolution.
Micro-calorimeter: Hf-STJ can generate enough quasi-particles from cooper pair breakings to achieve 2% energy resolution for photons with Eg = 25meV.
I-V curve of Hf-STJ (100x100m2 )
T~40mK, Ic=10μA, Rd=0.6Ω
B=0 Gauss
B=10 Gauss
Direct wire bonding on Hf layer
STJ size | # of samples | Rd
200 x 200μm2 | 3 | 0.22±0.01 Ω
100 x 100 μm2 | 3 | 0.60±0.10 Ω

## Slide 38
In 2016, we made a thin aluminum layer (9nm) on the HfO layer (1-2 nm) to improve the insulation of the HfOX layer. Hf/Al/HfOX/Hf-STJ
Latest Results of Hf-STJ R&D
Hf
HfOX
Al(9nm)
Ileak = 5μA at 10μV.
Rd = 2Ω
Dynamic Resistance was improved by a factor of 15 in Hf/Al/HfOX/Hf-STJ.

## Slide 39
Hf/Al/HfOX/Hf-STJ reduced the leakage current to one-fourth.
By making the size smaller, we will be able to decrease the leakage current by a factor of 1/400.
By decreasing the operation temperature, we will be able to decrease the leakage current significantly.
Leakage Current of Hf-STJ

## Slide 40
Response of Hf-STJ to Laser Pulse Light
Visible light laser (λ=465nm) 10Hz duration
Response speed (120μs) is slower than Nb/Al-STJ response speed ( around a fewμs).
Hf/Al/HfOX/Hf-STJ

## Slide 41: Schedule
41
41
Nb/Al-STJ設計・開発
 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Experiment Design |  |  |  |  |  | 
Superconducting Tunnel Junction (STJ ) Detector |  |  |  |  |  | 
Preamplifier at 1K and Post-Preamp (Fermilab, JAXA, KEK, AIST, Tsukuba） |  |  |  |  |  | 
Dispersive Element, Optics |  |  |  |  |  | 
Cryostat |  |  |  |  |  | 
Measurements＋Analysis |  |  |  |  |  | 
Experiment design with FIR Rocket
Experiment design with Satellite such as SPICA
R&D
of Nb/Al-STJ
Production
Production
Design and R&D
Simulation
Design and R&D
Design and R&D of Hf-STJ Detector (for Satellite Experiment)
Production
Analysis Program
Analysis
Design and R&D
Production
Far-Infrared Observatory Rocket Experiment
Design, R&D, Production
Design, R&D, Production
Design, R&D, Production

## Slide 42
Research Core for the History of the Universe
under Center for integrated Research in Fundamental Science and Engineering,
University of Tsukuba (founded on Sep. 1, 2014)
Mission: coordinate the studies in elementary particles, quark nuclear matters and astrophysics to construct an integrated view of the History of the Universe.
Simulation of the Universe Evolution
Superstring
Cosmic Neutrino Background
Dark Galaxies
Lattice QCD
Creation of Structure
Matter Evolution
Higgs Particle
Neutrino
Quark Gluon Plasma
Critical Point
Genesis of Matters
Mass Origin
Force Origin
Illuminate the “Darkness”:
=>Dark matter, Dark energy , Dark galaxies
=>Genesis of matters, creation of structure and their evolution

## Slide 43: Schedule of Research Core for the History of the Universe
These five projects were approved as large research projects in Master Plan 2017 by Science Council of Japan.
Cosmic Background Neutrino
Antarctic Astronomy
Higgs
Unstable Nuclei
Quark Gluon Plasma
Simulation on Universe Evolution

## Slide 44: Research Core for the History of the Universe Tomonaga Center for the History of the Universe Re-Organization
From Oct. 2017
Cosmic Background Neutrino
Antarctic Astronomy
Higgs (ATLAS)
Unstable Nuclei
Quark Gluon Plasma
Particle Detector R&D
Approved for October 2017 to March 2022 (10,500kYen/year).
Budget for Postdocs, Detector R&D and travel expenses.

## Slide 45: R&D Budgets for the COBAND in the period of JFY2013-2017
Chart: 
| Grant in Aid from MEXT | University Support | KEK Support | Japan-US
 | 77.5 | 21 | 5 | 17
Grant in Aid “Neutrino” from MEXT | R&D of Superconducting Infrared Detector for Neutrino Decay Experiment | JFY2013－2017 | 77.5 MYen
University Support | 3He Sorption Refrigerator | JFY2013, 2016 | 21.0 MYen
KEK Support | Cooperative Project of University of Tsukuba and KEK | JFY2013-2016 | 5.0 MYen
Japan-US Project | Neutrino Decay Search Experiment Cooperative | JFY2012-2014 | 17.0 MYen
Total : 120.5Myen
(~ $1.1M)

## Slide 46: Summary
R&D of STJ detectors and the design of the COBAND rocket experiment are underway.
          Determination of the neutrino mass
                origin of elementary particle mass spectra
      Discovery of the cosmic background neutrino
            new probe of the very early universe
New far-infrared photon detector is being developed:
      Nb/Al-STJ satisfied our requirement for leakage current less than 0.1pA
      Cryogenic amplifier with the SOI technology worked at 300mK
      We have succeeded in amplifying the STJ signal with the SOI cryogenic amplifier.
      Aiming at one photon detection in the far-infrared range
      applicable to the other fields such as X-ray energy measurement with higher energy resolution.
      COBAND WEB page http://hep.px.tsukuba.ac.jp/coband/eng/

## Slide 47: People who will join COBAND collaboration are very welcome. Please join us.

## Slide 48: BACKUP

## Slide 49: Cosmic Background Neutrino
Temperature:
Below 3MeV, ν is decoupled from other particles because the weak interaction cross section becomes too small.
Below 1MeV, e+e- →γγ is possible, but γγ→e+e- is impossible. so photons are reheated by this process. The entropies before and after this time are equal to each other:
g=2( for γ), 2( for e- or e+), 1(for ν or anti-ν)
where g is the spin degree of freedom, and F = 1( for fermions) and 0 (for bosons).
The present entropies of photons and neutrinos, and are given by
→ = = 1.95K
where + for fermions and - for bosons, and E is energy and μ is a chemical potential.
For μ and m T,
Energy density
Number density n =
Entropy

## Slide 50: Cosmic Background Neutrino
Temperature:
= 1.95K
Number density:
As μ/T ≪1，
where g is the spin degree of freedom, and F = 1( for fermions) and 0 (for bosons).
→ =

## Slide 51: Prototype of Cryostat for the Rocket Experiment
Made by Jeck Tohri company.
In April 2017, a prototype of the cryostat for the rocket experiment was made. This is a 3He sorption 0.3K refrigerator inside of 4He depressurized 1.8K refrigerator. (For now it does not have a 3He sorption 0.3K refrigerator inside yet.)
We will test Nb/Al-STJ inside of this cryostat with far-infrared(50μ) photon beam at Fukui this winter.

## Slide 52: Near-Infrared Photon Energy Spectrum from Outer Space
April 2017 (Press Release): CIBER rocket experiment measured the energy spectrum of the cosmic infrared background (CIB) in the near-infrared region. They found an excess of the CIB spectrum over the prediction by integrated galaxy light (IGL).
This excess might be due to first-generation stars Ly-α.
CIBER collaboration plans to do CIBER-2 rocket experiment which has 10 times larger sensitivity.
Integrated Galaxy Light (IGL)
CIBER Extragalactic Background Light (EBL)

## Slide 53: Astrophysics with NIR and FIR by AKARI
NIR Middle-IR Far-IR
NIR and FIR from interstellar gas → Formation and evolution of galaxies, stars and dusts
NIR: Search for first-generation stars using Ly-α line.
FIR: Search for first-generation heavy element dusts.
3 4 7 11 15 24 65 90 140 λ(μm)
Map of NIR from Milky Way Galaxy measured by AKARI
Molecular cloud IR in the arm of NGC1313 measured by AKARI

## Slide 54: Performance of Nb/Al-STJ in SOI-STJ Detector
2 mV /DIV.
1 mA /DIV.
500μV /DIV.
10 nA /DIV.
2mV /DIV.
50μA /DIV.
2 mV /DIV.
1 mA /DIV.
Ic～200μA
Ｅｎｌａｒｇｅｄ
We measured the I-V curve of the Nb/Al-STJ (50 x 50μm2 junction) processed on the SOI wafer
at 700mK with a dilution refrigerator.
I-V curve of Josephson Junction
Quality Factor (Rdynamic/Rnormal)
On Si wafer : 5 x 105
On SOI wafer : 3 x 105
B=35 G
Ｅｎｌａｒｇｅｄ

## Slide 55
Performance of SOIFET at Cryogenic Temperature
Saturating current is higher as the temperature becomes lower.
Non-linearity was found at cryogenic temperature near threshold region. This problem was solved by improving LDD(Lightly Doped Drain).
At cryogenic temperature (3K),
Threshold rise in Ids-Vds curve become much sharper.
Subthreshold current is suppressed.
̶̶ ROOM
̶̶̶ 3K
Vds (V)
Ids (A)
Vgs (V)
Ids (A)
̶̶ ROOM
̶̶̶ 3K

## Slide 56
Test Results of the cryogenic SOI preamplifier
Amplifier gains are around 50 both at room temperature and 3K with adjusted bias voltages of M2.
Bandwidth of buffer is enough high for the amplifier of STJ signal (up to 200kHz) both at room temperature and 3K.
Amplifier
Buffer

## Slide 57: STJ response at a constant current mode
STJ has a large resistance in series.
→ constant current mode
STJ response to light is observed as a voltage drop.
I
V
STJ I-V curve w/light w/o light
V0=V+RI
~1mV
Laser light pulse
V
R=1M~100M
High impedance voltage amplifier
STJ
CSTJ
I=I(V)
V0

## Slide 58: Development of SOI Charge sensitive preamplifier (SOISTJ5)
STJ capacitance is not so small ( 20pF for 20μm square STJ).
STJ response speed is a few μsec.
STJ operation at a constant voltage mode is favorable.
  → Low input impedance
  charge amplifier
  operational for 1MHz.

## Slide 59: Op-amp Circuit for STJ (SOI-STJ5 design)
Buffer stage
Telescopic cascode
Bias
telescopic cascode differential amplifier
Feedback C=2pF x R=5MOhm = 10s
Power consumption ~150W
Iref
Iref
Iref
Iref2
10/10
W(m)/L(m)
10/10
10/10
20/10
12/7
100/7
100/7
100/1
100/1
4/1
4/1
2/10
4/10
4/10
VDD=-VSS=1.5V
Iref>10A
Iref/5
Iref2/5
Iref2/5
This cryogenic charge amplifier test is now underway.

## Slide 60: COBAND Collaboration ( Cosmic Background Neutrino Decay Search)
2007 Univ. of Tsukuba, JAXA/ISAS, RIKEN, KEK, Seoul National Univ.
A part of the consortium of the History of the Universe
Univ. of Tsukuba
S. H. Kim, Y. Takeuchi
STJ detector,
Electronics,
Cryostat, Optical system
Kwansei Gakuin Univ.
S. Matsuura
Cryostat, Optical system
KEK
Y. Arai, M. Hazumi
Electronics
Kindai Univ.
Y. Kato
Data transfer
RIKEN
S. Mima
STJ detector
Okayama Univ.
H. Ishino
STJ detector
Fukui Univ.
T. Yoshida
FIR photon beam source
FNAL
E. Ramberg
Electronics
Seoul National Univ.
S. B. Kim
STJ detector
AIST
M. Ohkubo, M. Ukibe
SOI-STJ detector
2011 FNAL, Okayama Univ., Fukui Univ., Kindai Univ.
2014 AIST
JAXA/ISAS
T. Wada, H. Ikeda
Rocket, Electronics
Kwansei Gakuin
Univ.
Shizuoka Univ.
S. Kawahito
Electronics
2015 Shizuoka Univ.